## Slide 1: Principles of Furniture & Joinery Design
Design process

## Slide 2: Furniture Design
When considering making a custom piece of furniture the design phase is probably more important than the manufacturing phase as this offers you the opportunity to experiment and perfect the design without wasting valuable materials and time.
There are many factors to take into consideration when designing custom furniture.
Task: Can you list some?

## Slide 3: Furniture Design
The period or style from which the design originates
The ergonomics of the furniture
The construction techniques used
The material characteristics
The type of finish to be applied
Cost?
Budget will determine many things

## Slide 4: Design steps & considerations
Determining the size and complexity of the project
Defining and applying furniture standards
Creating ideas on paper including sketches and drawing
Creating mock-ups or scale representations of the furniture
(mock-ups can consist of cardboard or small scale models which can be used to provide an visual idea of the proportions and design)

## Slide 5: Design steps & considerations
Examine the mechanics of the design
Developing your design
Assess the demands of the recipient of the furniture, be it yourself or a client.
Form and function should be incorporated into the design
The design should be customized specifically for the intended use and also for the recipients' wishes.

## Slide 6: Design Objectives
Function: How will this furniture be used?
Proportion: What size will it be?
Customize: Who will use it?
Location: Where will it be placed?
Style: What should it look like?
Visual impact: What should this be?
To complement or contrast the surrounding furniture.
Is it to be a focal piece or to blend in with surroundings
Should it enclose (hide) or showcase its contents

## Slide 7: Design Proportions
Consider both function and form in your design
Are the components of the design to be large... or small and fine
Positive and negative shapes and areas
Design furniture to complement other furniture in the room or alternatively, to contrast with surrounding furniture
Begin with known, proven design standards (Golden rule or mean)
Task: The Golden Rectangle
A B

## Slide 8: Golden Ratio
Pleasing ratios which have been used by master architects, painters, and implemented in furniture design throughout the ages.
This ratio of numbers was discovered by An Italian man Leonardo Fibonacci. (1170 – 1250)
If you add 1+1=2, 1+2=3, 2+3=5, 3+5=8, 5+8=13 and so on you will get a sequence of numbers, 1,2,3,5,8,13, . .
If you divide any of these numbers by the number preceding it you will get 1.618
Golden number or mean is 1.618

## Slide 9: Golden section (rectangle)
If top measures 800mm then the width should measure 800 ÷ 1.618 = 494
Using this ratio the most pleasing size would be 800mm x 495mm
The golden rectangle is a proportioning guideline for anything rectangular.
Task: Without using measurements draw a rectangle.
Now measure the longest side.
Divide this measurement by 1.618.
Now measure the shortest side and see how close you are to that number.
Or divide sides to get 1.618 as answer
https://youtu.be/c8ccsE_IumM

## Slide 10: Design Proportions
Can you base your furniture design on a previous style or period
(Chippendale, Hepplewhite, Federal, Shaker, Art Nouveau)
Most styles throughout history stem from or are influenced by Greek & Roman architecture. This is true in both furniture and joinery styles.
Develop the furniture design in its entirety
Break the design down and incorporate detail into the individual components and groupings of components of the furniture.

## Slide 11: The complexity of the furniture design.
How much time will be consumed in creating this piece of furniture?
Do you have the necessary skills?
Do you have the necessary expertise to undertake the project?
Are you sufficiently equipped to undertake the crafting of this furniture design?
How large is the furniture, do you have sufficient space to be able to manufacture it?

## Slide 12: The furniture you are designing.
Is the furniture design adapted from a previous style?
Can you apply elements from a previous style or period into your design?
What are the resources you might use to derive a furniture design?
(woodworking publications, woodworking books, pattern books)
Online design sites (houzz.com) online catalogues, auction house websites etc.
Is it ok to adapt a pre-existing style and design to meet your objectives?

## Slide 13: Furniture Proportions
The assembly of all the individual components of your design, with aesthetics, proportion and symmetry all being considered.
The height to width to depth ratio for your furniture design are factors which form the design proportions.
Always bear your clients requirements in mind when designing custom furniture , remember recommended standards are based on the size of the average person.

## Slide 14: Logical sequence of design
Create concept sketches (use each successive sketch as a basis for a new idea or extract an element of the sketch to be added to design)
Create a rough drawing of the design from the sketch with the major proportions, scale, and elements of the design described.
Important KEEP all sketches. Keep all designs, concepts and ideas together in a folder. Hoard everything.

## Slide 15: Logical sequence of design
An orthographic drawing (working drawings) include key measurements, and specifications.
You can go on to create a full scale drawing of the furniture design. This will enable you to have accurate drawings of the individual components of the design for manufacturing of the furniture components.
Task: Look around your house and choose 5 items of furniture that you like and measure the top, front and sides to determine if they fit within the Golden ratio.